## Slide 1: HNDIT1032 Computer and Network Systems
Week 12- Data Communication & Computer Network

## Slide 2: Introduction
This chapter provides an introduction to Computer networks and covers fundamental topics like data, information to the definition of communication and computer networks.
The main objective of data communication and networking is to enable seamless exchange of data between any two points in the world.

## Slide 3: Data Communications
Data Communication is a process of exchanging data or information In case of computer networks this exchange is done between two devices over a transmission medium.
This process involves a communication system which is made up of hardware and software.

## Slide 4: Characteristic of Data Communication
The effectiveness of any data communications system depends upon the following three fundamental characteristics
  Delivery
  Accuracy
  Timeliness
  Jitter

## Slide 5: Components of Data Communication
Message
Sender
Receiver
Medium
Protocol

## Slide 6: Data Flow
Two devices communicate with each other by sending and receiving data. The data can flow between the two devices in the following ways.
  Simplex
  Half Duplex
  Full Duplex

## Slide 7: Simplex
In Simplex, communication is unidirectional Only one of the devices sends the data and the other one only receives the data.
Example: in the above diagram: a cpu send data while a monitor only receives data.

## Slide 8: Half Duplex
In half duplex both the stations can transmit as well as receive but not at the same time.
When one device is sending other can only receive and vice versa (as shown in figure above.) Example: A walkie-talkie.

## Slide 9: Full Duplex
In Full duplex mode, both stations can transmit and receive at the same time.
Example: mobile phones

## Slide 10: Computer Network
A computer network can be defined as a collection of nodes.
A node can be any device capable of transmitting or receiving data.
The communicating nodes have to be connected by communication links.
Computer Networks are used for data communications.

## Slide 11: Categories of Network
Networks are categorized on the basis of their size. The three basic categories of computer networks are:
  Local Area Network (LAN)
  Metropolitan Area Network (MAN)
  Wide Area Network (WAN).

## Slide 12: Local Area Network
LAN connects computers in a small area like a room, building, office or a campus spread up to a few kilometers.
They are privately owned networks, with a purpose to share resources and to exchange information.
The computers in a LAN are generally connected using cables.

## Slide 13: Example-LAN

## Slide 14: Wide Area Network
WAN is a network that connects computers over long distances like cities, countries, continents, or worldwide .
WAN uses public, leased, or private communication links to spread over long distances.
WAN uses telephone lines, satellite link, and radio link to connect.

## Slide 15: Example-WAN

## Slide 16: Metropolitan Area Network
MAN is a computer network spread over a city. Cable television network is an example of MAN.
The computers in a MAN are connected using coaxial cables or fiber optic cables.
MAN also connects several LAN spread over a city

## Slide 17: Example-MAN

## Slide 18: Advantages of Computer Networks
Central usage of data
Anyone can connect
Data Sharing
Flexible
Reliable

## Slide 19: Disadvantages
Cost of network
Virus and malware
Robustness
Lack of indepence

## Slide 20: Data & Signal
To be transmitted, data must be transformed to electromagnetic signals.
Signal can be
  Analog
  Digital

## Slide 21: Analog Signal
An analog signal has infinitely many levels of intensity over a period of time.
A simple analog signal is a sine wave that cannot be further decomposed into simpler signals.

## Slide 22: Characteristic of Analog Signal
A sine wave is characterized by three parameters:
  Peak Amplitude
  Frequency
  Phase

## Slide 23: Peak Amplitude

## Slide 24: Frequency
Frequency refers to the number of cycles completed by the wave in one second.
Period refers to the time taken by the wave to complete one second.

## Slide 25: Phase

## Slide 26: Relation between Frequency & Period

## Slide 27: Wavelength
The wavelength of a signal refers to the relationship between frequency (or period) and propagation speed of the wave through a medium.
The wavelength is the distance a signal travels in one period.

## Slide 28: Digital Signal
A digital is a signal that has discrete values.
The signal will have value that is not continuous.
Information in a digital signal can be represented in the form of voltage levels.

## Slide 29: Bit Interval
It is the time required to send one bit.
It is measured in seconds

## Slide 30: Bit Rate
It is the number of bits transmitted in one second.
It is expressed as bits per second (bps).
Relation between bit rate and bit interval can be as follows.

## Slide 31: Baud Rate
It is the rate of Signal Speed, i.e the rate at which the signal changes.
A digital signal with two levels ‗0‘ & ‗1‘ will have the same baud rate and bit rate & bit rate.

## Slide 32: Transmission of Digital Signal
Baseband Transmission-The signal is transmitted without making any change to it (ie. Without modulation)
Broadband Transmission-In broadband transmission we use modulation, i.e we change the signal to analog signal before transmitting it

## Slide 33: Bandwidth of a Signal
Bandwidth can be defined as the portion of the electromagnetic spectrum occupied by the signal.
It may also be defined as the frequency range over which a signal is transmitted.

## Slide 34: Example-Bandwidth

## Slide 35: References
Clements, A., The Principles of Computer Hardware, Oxford University Press (4th Ed), 2006.